## Slide 1: Data Communication CSE 315
Dr. A.K.M. Muzahidul Islam
Professor
Computer Science & Engineering (CSE)
United International University (UIU)
Fall 2018

## Slide 2: Schedule
  Section ‘B’
    Sat/Tuesday
      11:40 a.m.~ 1:10 p.m.
      Room No. 0332 (Level 3)
    Counseling
      14:00 p.m.~ 16:00 p.m.
      Room No. 333/D (Level 3)
  Section ‘C’
    Sun/Wednesday
      1:30 p.m.~ 3:00 p.m.
      Room No. 0328 (Level 3)
    Counseling
      11:00 p.m.~ 13:00 p.m.
      Room No. 333/D (Level 3)

## Slide 3: Assessment
  Attendance : 5%
  Assignments : 5%
  Class Tests : 20%
  Mid Term : 30%
  Final : 40%
Grading Policy
  A (Plain) : 90-100 C+ (Plus) : 70-73
  A- (Minus) : 86-89 C (Plain) : 66-69
  B+ (Plus) : 82-85 C- (Minus) : 62-65
  B (Plain) : 78-81 D+ (Plus) : 58-61
  B- (Minus) : 74-77 D (Plain) : 55-57

## Slide 4: Resources
Data Communications and Networking. Behrouz A. Forouzan
Data and Computer Communications. William Stallings (TENTH EDITION)
Modern Digitial and Analog Communication Systems. BP-Lathi Zhi Ding (4th edition)
Computer Networks Andrew S. Tanenbaum

## Slide 5: Outline
Transmission Terminology
Guided Media
Unguided or Wireless Media
Summary

## Slide 6: Transmission Terminology
Data transmission occurs between Transmitter Tx and Receiver Rx over some transmission medium:
  Transmission Medium: Guided or Unguided.
  In both cases, communication is in the form of electromagnetic waves.
Guided media
  The waves are guided along a physical path.
  Ex. Twisted pair, coaxial cable, and optical fiber.
Unguided media or Wireless media
  Provides a means for transmitting electromagnetic waves but Do Not guide them;
  Ex. propagation through air, vacuum, and seawater.
Notes: Data transmission occurs between transmitter and receiver over some transmission
medium. Transmission media may be classified as guided or unguided. In both
cases, communication is in the form of electromagnetic waves. With guided media ,
the waves are guided along a physical path; examples of guided media are twisted
pair, coaxial cable, and optical fiber. Unguided media , also called wireless , provide
a means for transmitting electromagnetic waves but do not guide them; examples
are propagation through air, vacuum, and seawater.

## Slide 7
As a function of time, an electromagnetic signal can be either analog or digital.
Analog signal :
The signal intensity varies in a smooth, or continuous , fashion over time.
There are no breaks or discontinuities in the signal. Example: Speech
Digital signal :
The signal intensity maintains a constant level for some period of time and then abruptly changes to another constant level, in a discrete fashion.
Example: binary 1s and 0s.
Notes: Viewed as a function of time, an electromagnetic signal
can be either analog or digital. An analog signal is one in which the signal intensity
varies in a smooth, or continuous , fashion over time. In other words, there are no
breaks or discontinuities in the signal. A digital signal is one in which the signal
intensity maintains a constant level for some period of time and then abruptly
changes to another constant level, in a discrete fashion. Figure 3.1 shows an example
of each kind of signal. The analog signal might represent speech, and the digital
signal might represent binary 1s and 0s.

## Slide 8
Periodic Signal : The simplest sort of signal, in which the same signal pattern repeats over time.
Figure 3.2 shows an example of a periodic continuous signal (sine wave) and a periodic discrete signal (square wave).
Mathematically a signal s(t) is defined to be periodically, iff
s ( t + T ) = s (t) - ∞ < t < +∞
In data communication, we commonly use periodic analog signals (because they need less bandwidth) and aperiodic digital signals (can present variation of data).
Notes: The simplest sort of signal is a periodic signal , in which the same signal pattern
repeats over time. Figure 3.2 shows an example of a periodic continuous signal (sine
wave) and a periodic discrete signal (square wave).

## Slide 9: Frequency, Spectrum, and Bandwidth
A Signal is transmitted by the Tx and transmitted over a medium
  The Signal is a function of Time
  The Signal can also be expressed as a function of Frequency
    i.e., consists component of different frequencies
Time Domain
  Signal Intensity vs Time
Frequency Domain
  Peak Signal Intensity of component vs Frequency
Frequency Domain view of a Signal is more important to an understanding of data transmission than a Time Domain.

## Slide 10
Time and frequency domains
An analog signal is best represented in the frequency domain.

## Slide 11: Sine Wave
Is the fundamental periodic signal
A Sine waves can be used to represent any
other waveform using Fourier Transforms.
Can be represented by three parameters
s(t) = A sin(2πft + ) Sinusoid
  Peak amplitude (A)
    Maximum value or strength of the signal over time
    Typically measured in volts
  Frequency (f)
    Rate at which the signal repeats
    Hertz (Hz) or cycles per second
    Period (T) is the amount of time for one repetition; T = 1/f
  Phase ()
    Relative position in time within a single period of signal
Notes: The sine wave is the fundamental periodic signal. A general sine wave can be
represented by three parameters: peak amplitude (A ), frequency (f ), and phase ( ).
The peak amplitude is the maximum value or strength of the signal over time; typically,
this value is measured in volts. The frequency is the rate [in cycles per second,
or hertz (Hz)] at which the signal repeats. An equivalent parameter is the period
(T ) of a signal, which is the amount of time it takes for one repetition; therefore,
T = 1/f . Phase is a measure of the relative position in time within a single period of a
signal, as is illustrated subsequently.

## Slide 12: The effect of varying A, f, 
The frequency is 1 Hz; thus the period is T = 1 second.
Has the same frequency and phase but a peak amplitude of 0.5.
We have f = 2, which is equivalent to T = 0.5.
The effect of a phase shift of π/4 radians, which is 45 degrees (2π radians = 360˚ = 1 period).
Notes: The general sine wave can be written
s(t) = A sin(2πft + f)
A function with the form of the preceding equation is known as a sinusoid. Figure 3.3 shows the effect of varying each of the three parameters. In part (a) of the figure, the frequency is 1 Hz; thus the period is T = 1 second. Part (b) has the same frequency and phase but a peak amplitude of 0.5. In part (c) we have f = 2, which is equivalent to T = 0.5. Finally, part (d) shows the effect of a phase shift of π/4 radians, which is 45 degrees (2π radians = 360˚ = 1 period).
InFigure 3.3, the horizontal axis is time; the graphs display the value of a signal at a given point in space as a function of time. These same graphs, with a change of scale, can apply with horizontal axes in space. In this case, the graphs display the value of a signal at a given point in time as a function of distance. For example, for a sinusoidal transmission (e.g., an electromagnetic radio wave some distance from a radio antenna, or sound some distance from a loudspeaker), at a particular instant of time, the intensity of the signal varies in a sinusoidal way as a function of distance from the source.

## Slide 13: Wavelength ()
The wavelength () of a signal -
distance occupied by a single cycle
Can also be stated as the distance between two points of corresponding phase of two consecutive cycles
Assuming signal velocity v, then the wavelength is related to the period as
 = vT
Or equivalently  = c/f ; T = 1/f
Especially when v=c
c = 3*108 m/s (speed of light in free space)
 = cT
Notes: There is a simple relationship between the two sine waves, one in time and one in space. The wavelength () of a signal is the distance occupied by a single cycle, or, put another way, the distance between two points of corresponding phase of two consecutive cycles. Assume that the signal is traveling wdith a velocity v. Then the wavelength is related to the period as follows: l = vT. Equivalently, lf = v. Of particular relevance to this discussion is the case where v = c, the speed of light in free space, which is approximately 3 ´ 108 m/s.

## Slide 14
Wavelength

## Slide 15: Spectrum and Bandwidth
Spectrum
Range of frequencies contained in signal
Absolute bandwidth
Width of spectrum
Effective bandwidth (or just bandwidth)
Set of Frequencies e.g., f, 3f, etc.
The bandwidth is 3f – f = 2f.
Effective bandwidth is the band within which most of the signal energy is concentrated.
Any transmission system (transmitter + medium + receiver) will be able to accommodate only a limited band of frequencies i.e., limits the data rate that can be carried on the transmission medium.
Notes: The spectrum of a signal is the range of frequencies that it contains. For the signal of Figure 3.4c, the spectrum extends from f to 3f. The absolute bandwidth of a signal is the width of the spectrum. In the case of Figure 3.4c, the bandwidth is 3f – f = 2f. Many signals, such as that of Figure 3.5b, have an infinite bandwidth. However, most of the energy in the signal is contained in a relatively narrow band of frequencies. This band is referred to as the effective bandwidth, or just bandwidth.
One final term to define is dc component. If a signal includes a component of zero frequency, that component is a direct current (dc) or constant component.

## Slide 16: Example 1
If a periodic signal is decomposed into five sine waves with frequencies of 100, 300, 500, 700, and 900 Hz, what is the bandwidth? Draw the spectrum, assuming all components have a maximum amplitude of 10 V
B = fh - fl = 900 - 100 = 800 Hz
The spectrum has only five spikes, at 100, 300, 500, 700, and 900 (see Figure 13.4 )

## Slide 17
Example 1

## Slide 18: Example 2
A signal has a bandwidth of 20 Hz. The highest frequency is 60 Hz. What is the lowest frequency? Draw the spectrum if the signal contains all integral frequencies of the same amplitude
B = fh - fl, 20 = 60 – fl, fl = 60 - 20 = 40 Hz

## Slide 19: Example 3
A signal has a spectrum with frequencies between 1000 and 2000 Hz (bandwidth of 1000 Hz). A medium can pass frequencies from 3000 to 4000 Hz (a bandwidth of 1000 Hz). Can this signal faithfully pass through this medium?
The answer is definitely no. Although the signal can have the same bandwidth (1000 Hz), the range does not overlap. The medium can only pass the frequencies between 3000 and 4000 Hz; the signal is totally lost.

## Slide 20: Summary
Advantages:
Increased bandwidth -> increased accuracy
Increased frequency -> increased data rate
Disadvantages:
Increased bandwidth -> increased cost
Increased frequency -> increased complexity (cost)
A designer chooses a signal that maximizes data rate, minimizes errors and minimizes cost.

## Slide 22
Earlier observed, analog signals,
used to represent analog data, and digital signals, used to represent digital data.
Digital data can also be represented by analog signals by use of a modem (modulator/demodulator).
The modem converts a series of binary (two-valued) voltage pulses into an analog signal by encoding the digital data onto a carrier frequency.
Analog data can be represented by digital signals. The device that performs this function for voice data is a codec (coder-decoder).
Notes: In the foregoing discussion, we have looked at analog signals,
used to represent analog data, and digital signals, used to represent digital
data. Generally, analog data are a function of time and occupy a limited frequency
spectrum; such data can be represented by an electromagnetic signal occupying the
same spectrum. Digital data can be represented by digital signals, with a different
voltage level for each of the two binary digits.
As Figure 3.13 illustrates, these are not the only possibilities. Digital data can
also be represented by analog signals by use of a modem (modulator/demodulator).
The modem converts a series of binary (two-valued) voltage pulses into an
analog signal by encoding the digital data onto a carrier frequency. The resulting
signal occupies a certain spectrum of frequency centered about the carrier and
may be propagated across a medium suitable for that carrier. The most common
modems represent digital data in the voice spectrum and hence allow those data to
be propagated over ordinary voice-grade telephone lines. At the other end of the
line, another modem demodulates the signal to recover the original data.
In an operation very similar to that performed by a modem, analog data can
be represented by digital signals. The device that performs this function for voice
data is a codec (coder-decoder). In essence, the codec takes an analog signal that
directly represents the voice data and approximates that signal by a bit stream. At
the receiving end, the bit stream is used to reconstruct the analog data.
Thus, Figure 3.13 suggests that data may be encoded into signals in a variety of
ways. We return to this topic in Chapter 5.

## Slide 23: Transmission Impairments
Signal received may differ from signal transmitted causing:
  Analog - degradation of signal quality
  Digital - bit errors
Most significant impairments are
  Attenuation and attenuation distortion
    Loss of Energy
    Signal strength falls off with distance over any transmission medium
  Delay distortion
    Signal changes its form or shape
    Signals’ arrival time vary
    Occurs in transmission cables such as twisted pair, coaxial cable, and optical fiber
    Does not occur when signals are transmitted through the air by means of antennas
  Noise
    Unwanted signals inserted between transmitter and receiver
Notes: With any communications system, the signal that is received may differ from the
signal that is transmitted, due to various transmission impairments. For analog signals,
these impairments introduce various random modifications that degrade the
signal quality. For digital signals, bit errors may be introduced, such that a binary 1
is transformed into a binary 0 or vice versa. In this section, we examine the various
impairments and how they may affect the information-carrying capacity of a communication
link; Chapter 5 looks at measures that can be taken to compensate for
these impairments.
The most significant impairments are
• Attenuation and attenuation distortion
• Delay distortion
• Noise

## Slide 24
DATA RATE LIMITS
A very important consideration in data communications is how fast we can send data, in bits per second, over a channel. Data rate depends on three factors:
1. The bandwidth available
2. The level of the signals we use
3. The quality of the channel (the level of noise)
Noiseless Channel: Nyquist Bit Rate
Noisy Channel: Shannon Capacity
Using Both Limits
Topics:

## Slide 25: Capacity of a System
The bit rate of a system increases with an increase in the number of signal levels we use to denote a symbol.
A symbol can consist of a single bit or “n” bits.
The number of signal levels = 2n.
As the number of levels goes up, the spacing between level decreases -> increasing the probability of an error occurring in the presence of transmission impairments.

## Slide 26: Nyquist Bandwidth
In the case of a channel that is noise free:
The limitation of data rate is simply the bandwidth of the signal
  If the rate of signal transmission is 2B then a signal with frequencies no greater than B is sufficient to carry the signal rate
  Given a bandwidth of B, the highest signal rate that can be carried is 2B
For binary signals, the data rate that can be supported by B Hz is 2B bps
With multilevel signaling, the Nyquist formula becomes: C = 2B log2M
Data rate can be increased by increasing the number of different signal elements
  This increases burden on receiver
  Noise and other impairments limit the practical value of M
Notes: To begin, let us consider the case of a channel that is noise free. In this environment, the limitation on data rate is simply the bandwidth of the signal. A formulation of this limitation, due to Nyquist, states that if the rate of signal transmission is 2B, then a signal with frequencies no greater than B is sufficient to carry the signal rate. The converse is also true: Given a bandwidth of B, the highest signal rate that can be carried is 2B. This limitation is due to the effect of intersymbol interference, such as is produced by delay distortion. The result is useful in the development of digital-to-analog encoding schemes and is, in essence, based on the same derivation as that of the sampling theorem, described in Appendix G.
Note that in the preceding paragraph, we referred to signal rate. If the signals to be transmitted are binary (two voltage levels), then the data rate that can be supported by B Hz is 2B bps. However, as we shall see in Chapter 5, signals with more than two levels can be used; that is, each signal element can represent more than one bit. For example, if four possible voltage levels are used as signals, then each signal element can represent two bits. With multilevel signaling, the Nyquist formulation becomes
C = 2B log2M
where M is the number of discrete signal or voltage levels.
So, for a given bandwidth, the data rate can be increased by increasing the number of different signal elements. However, this places an increased burden on the receiver: Instead of distinguishing one of two possible signal elements during each signal time, it must distinguish one of M possible signal elements. Noise and other impairments on the transmission line will limit the practical value of M.

## Slide 27
Increasing the levels of a signal increases the probability of an error occurring.
In other words, it reduces the reliability of the system.

## Slide 28: Nyquist Theorem
Nyquist gives the upper bound for the bit rate of a transmission system by calculating the bit rate directly from the number of bits in a symbol (or signal levels) and the bandwidth of the system (assuming 2 symbols/per cycle).
Nyquist theorem states that for a noiseless channel:
C = 2 B log22n
C= capacity in bps
B = bandwidth in Hz

## Slide 29
Consider a noiseless channel with a bandwidth of 3000 Hz transmitting a signal with two signal levels. The maximum bit rate can be calculated as
Example 1

## Slide 30
Consider the same noiseless channel transmitting a signal with four signal levels (for each level, we send 2 bits). The maximum bit rate can be calculated as
Example 2

## Slide 31
We need to send 265 kbps over a noiseless channel with a bandwidth of 20 kHz. How many signal levels do we need?
Solution
We can use the Nyquist formula as shown:
Example 3
Since this result is not a power of 2, we need to either increase the number of levels or reduce the bit rate. If we have 128 levels, the bit rate is 280 kbps. If we have 64 levels, the bit rate is 240 kbps.

## Slide 32: Shannon Capacity Formula
Considering the relation of data rate, noise and error rate:
  Faster data rate shortens each bit so bursts of noise corrupts more bits
  Given noise level, higher rates mean higher errors
Shannon developed formula relating these to signal to noise ratio (in decibels)
  SNRdb=10 log10 (signal/noise)
  Capacity C = B log2(1+SNR)
  Theoretical maximumcapacity
  Get much lower rates in practice
Notes: Nyquist's formula indicates that, all other things being equal, doubling the bandwidth doubles the data rate. Now consider the relationship among data rate, noise, and error rate. The presence of noise can corrupt one or more bits. If the data rate is increased, then the bits become "shorter" so that more bits are affected by a given pattern of noise.
Figure 3.15 illustrates this relationship. If the data rate is increased, then more bits will occur during the interval of a noise spike, and hence more errors will occur.
All of these concepts can be tied together neatly in a formula developed by the mathematician Claude Shannon. As we have just illustrated, the higher the data rate, the more damage that unwanted noise can do. For a given level of noise, we would expect that a greater signal strength would improve the ability to receive data correctly in the presence of noise. The key parameter involved in this reasoning is the signal-to-noise ratio (SNR, or S/N), which is the ratio of the power in a signal to the power contained in the noise that is present at a particular point in the transmission. Typically, this ratio is measured at a receiver, because it is at this point that an attempt is made to process the signal and recover the data. For convenience, this ratio is often reported in decibels:
The signal-to-noise ratio is important in the transmission of digital data because it sets the upper bound on the achievable data rate. Shannon's result is that the maximum channel capacity, in bits per second, obeys the equation
C = B log2 (1 + SNR) (3.1)
where C is the capacity of the channel in bits per second and B is the bandwidth of the channel in hertz. The Shannon formula represents the theoretical maximum that can be achieved. In practice, however, only much lower rates are achieved. One reason for this is that the formula assumes white noise (thermal noise). Impulse noise is not accounted for, nor are attenuation distortion or delay distortion. Even in an ideal white noise environment, present technology still cannot achieve Shannon capacity due to encoding issues, such as coding length and complexity.
The capacity indicated in the preceding equation is referred to as the error-free capacity. Shannon proved that if the actual information rate on a channel is less than the error-free capacity, then it is theoretically possible to use a suitable signal code to achieve error-free transmission through the channel. Shannon's theorem unfortunately does not suggest a means for finding such codes, but it does provide a yardstick by which the performance of practical communication schemes may be measured.
Several other observations concerning the preceding equation may be instructive. For a given level of noise, it would appear that the data rate could be increased by increasing either signal strength or bandwidth. However, as the signal strength increases, so do the effects of nonlinearities in the system, leading to an increase in intermodulation noise. Note also that, because noise is assumed to be white, the wider the bandwidth, the more noise is admitted to the system. Thus, as B increases, SNR decreases.
The Expression Eb/N0
Finally, we mention a parameter related to SNR that is more convenient for determining digital data rates and error rates and that is the standard quality measure for digital communication system performance. The parameter is the ratio of signal energy per bit to noise power density per hertz, Eb/N0. Consider a signal, digital or analog, that contains binary digital data transmitted at a certain bit rate R. Recalling that 1 watt = 1 J/s, the energy per bit in a signal is given by Eb = STb, where S is the signal power and Tb is the time required to send one bit. The data rate R is just R = 1/Tb.
The ratio Eb/N0 is important because the bit error rate for digital data is a (decreasing) function of this ratio. Given a value of Eb/N0 needed to achieve a desired error rate, the parameters in the preceding formula may be selected. Note that as the bit rate R increases, the transmitted signal power, relative to noise, must increase to maintain the required Eb/N0.
Let us try to grasp this result intuitively by considering again Figure 3.15. The signal here is digital, but the reasoning would be the same for an analog signal. In several instances, the noise is sufficient to alter the value of a bit. If the data rate were doubled, the bits would be more tightly packed together, and the same passage of noise might destroy two bits. Thus, for constant signal to noise ratio, an increase in data rate increases the error rate.
The advantage of Eb/N0 over SNR is that the latter quantity depends on the bandwidth.

## Slide 33: Shannon’s Theorem
Shannon’s theorem gives the capacity of a system in the presence of noise.
C = B log2(1 + SNR)

## Slide 34
Consider an extremely noisy channel in which the value of the signal-to-noise ratio is almost zero. In other words, the noise is so strong that the signal is faint. For this channel the capacity C is calculated as
Example 4
This means that the capacity of this channel is zero regardless of the bandwidth. In other words, we cannot receive any data through this channel.

## Slide 35
We can calculate the theoretical highest bit rate of a regular telephone line. A telephone line normally has a bandwidth of 3000. The signal-to-noise ratio is usually 3162. For this channel the capacity is calculated as
Example 5
This means that the highest bit rate for a telephone line is 34.860 kbps. If we want to send data faster than this, we can either increase the bandwidth of the line or improve the signal-to-noise ratio.

## Slide 36
The signal-to-noise ratio is often given in decibels. Assume that SNRdB = 36 and the channel bandwidth is 2 MHz. The theoretical channel capacity can be calculated as
Example 6

## Slide 37
For practical purposes, when the SNR is very high, we can assume that SNR + 1 is almost the same as SNR. In these cases, the theoretical channel capacity can be simplified to
Example 7
For example, we can calculate the theoretical capacity of the previous example as

## Slide 38
We have a channel with a 1-MHz bandwidth. The SNR for this channel is 63. What are the appropriate bit rate and signal level?
Solution
First, we use the Shannon formula to find the upper limit.
Example 8

## Slide 39
The Shannon formula gives us 6 Mbps, the upper limit. For better performance we choose something lower, 4 Mbps, for example. Then we use the Nyquist formula to find the number of signal levels.
Example 8 (continued)

## Slide 40
The Shannon capacity gives us the upper limit;
the Nyquist formula tells us how many signal levels we need.

## Slide 42
Electromagnetic Spectrum
For Telecommunications
Figure 4.1 depicts the electromagnetic spectrum and indicates the frequencies
at which various guided media and unguided transmission techniques operate.
Notes: Figure 4.1 depicts the electromagnetic spectrum and indicates the frequencies
at which various guided media and unguided transmission techniques operate.
In this chapter, we examine these guided and unguided alternatives. In all cases,
we describe the systems physically, briefly discuss applications, and summarize key
transmission characteristics.

## Slide 43
The three guided media commonly used for data transmission:
(1) Twisted pair,
(2) Coaxial cable
(3) Optical fiber
Notes: The three guided media commonly used for data transmission are twisted pair,
coaxial cable, and optical fiber (Figure 4.2). We examine each of these in turn.

## Slide 44: Twisted Pair
Twisted pair is the least expensive and most widely used guided transmission medium
  Consists of two insulated copper wires arranged in a regular spiral pattern
  A wire pair acts as a single communication link
  Pairs are bundled together into a cable
  Most commonly used in the telephone network and for communications within buildings
Notes: The least expensive and most widely used guided transmission medium is twisted pair.
A twisted pair consists of two insulated copper wires arranged in a regular spiral pattern. A wire pair acts as a single communication link. Typically, a number of these pairs are bundled together into a cable by wrapping them in a tough protective sheath, or jacket. Over longer distances, cables may contain hundreds of pairs. The twisting tends to decrease the crosstalk interference between adjacent pairs in a cable. Neighboring pairs in a bundle typically have somewhat different twist lengths to reduce the crosstalk interference. On long-distance links, the twist length typically varies from 5 to 15 cm. The wires in a pair have thicknesses of from 0.4 to 0.9 mm.
By far the most common guided transmission medium for both analog and digital signals is twisted pair. It is the most commonly used medium in the telephone network and is the workhorse for communications within buildings.
In the telephone system, individual residential telephone sets are connected to the local telephone exchange, or "end office," by twisted-pair wire. These are referred to as subscriber loops. Within an office building, each telephone is also connected to a twisted pair, which goes to the in-house private branch exchange (PBX) system or to a Centrex facility at the end office. These twisted-pair installations were designed to support voice traffic using analog signaling. However, by means of a modem, these facilities can handle digital data traffic at modest data rates.
Twisted pair is also the most common medium used for digital signaling. For connections to a digital data switch or digital PBX within a building, a data rate of 64 kbps is common. Ethernet operating over twisted-pair cabling is commonly used within a building for local area networks supporting personal computers. Data rates for Ethernet products are typically in the neighborhood of 100 Mbps to 1 Gbps. Emerging twisted-pair cabling Ethernet technology can support data rates of 10Gbps. For long-distance applications, twisted pair can be used at data rates of 4 Mbps or more.
Twisted pair is much less expensive than the other commonly used guided transmission media (coaxial cable, optical fiber) and is easier to work with.

## Slide 45: Unshielded and Shielded Twisted Pair
Unshielded Twisted Pair (UTP)
Subject to external electromagnetic interference
Shielded Twisted Pair (STP)
Has metal braid or sheathing that reduces interference
Provides better performance at higher data rates
More expensive
Ordinary telephone wire
Consists of one or more twisted-pair cables, typically enclosed within an overall thermoplastic jacket which provides no electromagnetic shielding
The tighter the twisting, the higher the supported transmission rate and the greater the cost per meter
Notes: Twisted pair comes in two varieties: unshielded and shielded. As the name implies, unshielded twisted pair (UTP) consists of one or more twisted-pair cables, typically enclosed within an overall thermoplastic jacket, which provides no electromagnetic shielding. The most common form of UTP is ordinary voice-grade telephone wire, which is pre-wired in residential and office buildings. For data transmission purposes, UTP may vary from voice-grade to very high-speed cable for local area networks (LANs). For high-speed LANs, UTP typically has four pairs of wires inside the jacket, with each pair twisted with a different number of twists per centimeter to help eliminate interference between adjacent pairs. The tighter the twisting, the higher the supported transmission rate and the greater the cost per meter.
Unshielded twisted pair is subject to external electromagnetic interference, including interference from nearby twisted pair and from noise generated in the environment. In an environment with a number of sources of potential interference (e.g., electric motors, wireless devices, and RF transmitters), shielded twisted pair (STP) may be a preferred solution. Shielded twisted pair cable is manufactured in three different configurations:
Each pair of wires is individually shielded with metallic foil, generally referred to as foil twisted pair (FTP).
2. There is a foil or braid shield inside the jacket covering all wires (as a group). This configuration is sometimes designated as screened twisted pair (F/UTP).
3.There is a shield around each individual pair, as well as around the entire group of wires. This is referred to as fully-shielded twisted pair or shielded/foil twisted pair (S/FTP).
The shielding reduces interference and provides better performance at higher data rates. However, it may be more expensive and installers familiar with UTP technology may be reluctant to work with a new media type.

## Slide 46: Coaxial Cable
Coaxial cable can be used over longer distances and support more stations on a shared line than twisted pair
  Consists of a hollow outer cylindrical conductor that surrounds a single inner wire conductor
  Is a versatile transmission medium used in a wide variety of applications e.g., TV distribution, long distance telephone transmission and LANs
Notes: Coaxial cable, like twisted pair, consists of two conductors, but is constructed differently to permit it to operate over a wider range of frequencies. It consists of a hollow outer cylindrical conductor that surrounds a single inner wire conductor (Figure 4.2b). The inner conductor is held in place by either regularly spaced insulating rings or a solid dielectric material. The outer conductor is covered with a jacket or shield. A single coaxial cable has a diameter of from 1 to 2.5 cm. Coaxial cable can be used over longer distances and support more stations on a shared line than twisted pair.
Coaxial cable is a versatile transmission medium, used in a wide variety of applications. The most important of these are
Television distribution
Long-distance telephone transmission
Short-run computer system links
Local area networks
Coaxial cable is widely used as a means of distributing TV signals to individual homes—cable TV. From its modest beginnings as Community Antenna Television (CATV), designed to provide service to remote areas, cable TV reaches almost as many homes and offices as the telephone. A cable TV system can carry dozens or even hundreds of TV channels at ranges up to a few tens of kilometers.
Coaxial cable has traditionally been an important part of the long-distance telephone network. Today, it faces increasing competition from optical fiber, terrestrial microwave, and satellite. Using frequency division multiplexing (FDM, see Chapter 8), a coaxial cable can carry over 10,000 voice channels simultaneously.
Coaxial cable is also commonly used for short-range connections between devices. Using digital signaling, coaxial cable can be used to provide high-speed I/O channels on computer systems.

## Slide 47: Optical Fiber
A Thin flexible medium capable of guiding an optical ray
  Various glasses and plastics can be used to make optical fibers
  Has a cylindrical shape with three sections
    core (8-62.5 μm) – innermost, consists of thin strands made of glass or plastic
    cladding (125 μm) – glass or plastic coating that surrounds the core to confine light.
    Jacket – Hard plastic coating that protects the glass from moisture and damage
  Widely used in long distance telecommunications
  Performance, price and advantages have made it popular to use
Notes: An optical fiber is a thin, flexible medium capable of
guiding an optical ray. Various glasses and plastics can be used to make optical
fibers. The lowest losses have been obtained using fibers of ultrapure fused silica.
Ultrapure fiber is difficult to manufacture; higher-loss multicomponent glass fibers
are more economical and still provide good performance. Plastic fiber is even less
costly and can be used for short-haul links, for which moderately high losses are
acceptable.
An optical fiber strand (also called an optical waveguide ) has a cylindrical
shape and consists of three concentric sections: the core, the cladding, and the
buffer coating (Figure 4.2c). The core is the innermost section and consists of
thin strands made of glass or plastic; the core has a diameter in the range of 8 to
62.5 μm. The core is surrounded by a cladding , which is a glass or plastic coating
that has optical properties different from those of the core and a diameter of
125 μm. The interface between the core and cladding acts as a reflector to confine
light that would otherwise escape the core. The outermost layer is the buffer
coating , which is a hard plastic coating that protects the glass from moisture and
physical damage.
Fiber optic cable provides protection to the fiber from stress during installation
and from the environment once it is installed. Cables may contain from only
one to hundreds of fibers inside. The outermost layer of the cable, surrounding one
or a bundle of fibers, is the jacket . The jacket is composed of plastic and other
materials, layered to protect against moisture, abrasion, crushing, and other environmental
dangers.
Optical fiber already enjoys considerable use in long-distance
telecommunications, and its use in military applications is growing. The continuing
improvements in performance and decline in prices, together with the inherent
advantages of optical fiber, have made it increasingly attractive for local area
networking.

## Slide 48: Optical Fiber - Benefits
Greater capacity
  Data rates of hundreds of Gbps over tens of kilometers
  Smaller size and lighter weight
  Considerably thinner than coaxial or twisted pair cable
  Reduces structural support requirements
Lower attenuation
Electromagnetic isolation
  Not vulnerable to interference, impulse noise, or crosstalk
  High degree of security from eavesdropping
Greater repeater spacing
  Lower cost and fewer sources of error
Notes: The following characteristics distinguish optical fiber from twisted pair
or coaxial cable:
• Greater capacity: The potential bandwidth, and hence data rate, of optical
fiber is immense; data rates of hundreds of Gbps over tens of kilometers have
been demonstrated. Compare this to the practical maximum of hundreds of
Mbps over about 1 km for coaxial cable and just a few Mbps over 1 km or up
to 100 Mbps to 10 Gbps over a few tens of meters for twisted pair.
• Smaller size and lighter weight: Optical fibers are considerably thinner than
coaxial cable or bundled twisted-pair cable—at least an order of magnitude
thinner for comparable information transmission capacity. For cramped conduits
in buildings and underground along public rights-of-way, the advantage
of small size is considerable. The corresponding reduction in weight reduces
structural support requirements.
• Lower attenuation: Attenuation is significantly lower for optical fiber than for
coaxial cable or twisted pair (Figure 4.3c) and is constant over a wide range.
• Electromagnetic isolation: Optical fiber systems are not affected by external
electromagnetic fields. Thus the system is not vulnerable to interference,
impulse noise, or crosstalk. By the same token, fibers do not radiate energy, so
there is little interference with other equipment and there is a high degree of
security from eavesdropping. In addition, fiber is inherently difficult to tap.
• Greater repeater spacing: Fewer repeaters mean lower cost and fewer sources
of error. The performance of optical fiber systems from this point of view has
been steadily improving. Repeater spacing in the tens of kilometers for optical
fiber is common, and repeater spacings of hundreds of kilometers have
been demonstrated. Coaxial and twisted-pair systems generally have repeaters
every few kilometers.

## Slide 49: Categories of Application
Five basic categories of application have become important for optical fiber:
  Long-haul trunks (i.e. long-distance link)
    Connects all central switches and long-distance switches
    Average 1500 km and 20k to 60k voice channels
  Metropolitan trunks
    Average 12 km and 100k voice channels
  Rural exchange trunks
    Links towns and villages 40km to 160 km and 5k voice channels
  Subscriber loops
    Link between central exchange to a subscriber i.e. home, office, etc.
  Local area networks
    100 Gbps and 1000s of stations are supported.
Notes: Five basic categories of application have become important for optical fiber:
• Long-haul trunks
• Metropolitan trunks
• Rural exchange trunks
• Subscriber loops
• Local area networks
Telephone networks were the first major users of fiber optics. Fiber optic links
were used to replace copper or digital radio links between telephone switches, beginning
with long-distance links, called long lines or long haul, where fiber’s distance
and bandwidth capabilities made fiber significantly more cost-effective. Optical
fiber is used to connect all central offices and long-distance switches because it has
thousands of times the bandwidth of copper wire and can carry signals hundreds
of times further before needing a repeater, making the cost of a phone connection
over fiber only a few percent of the cost of the same connection on copper.
Long-haul routes average about 1500 km in length and offer high capacity (typically
20,000 to 60,000 voice channels). Undersea optical fiber cables have also enjoyed
increasing use.
Metropolitan trunking circuits have an average length of 12 km and may have
as many as 100,000 voice channels in a trunk group. Most facilities are installed in
underground conduits and are repeaterless, joining telephone exchanges in a metropolitan
or city area. Included in this category are routes that link long-haul microwave
facilities that terminate at a city perimeter to the main telephone exchange
building downtown.
Rural exchange trunks have circuit lengths ranging from 40 to 160 km that
link towns and villages. In the United States, they often connect the exchanges of
different telephone companies. Most of these systems have fewer than 5000 voice
channels. With the exception of some rugged or remote locations, the entire telephone
backbone is now optical fiber. Cables on the land are run underground or
aerially, depending on the geography and local regulations. Connections around
the world are run primarily on undersea cables, which now link every continent and
most island nations with the exception of Antarctica.
Subscriber loop circuits are fibers that run directly from the central exchange
to a subscriber. These facilities are beginning to displace twisted pair and coaxial
cable links as the telephone networks evolve into full-service networks capable of
handling not only voice and data, but also image and video. The initial penetration
of optical fiber in this application has been for the business subscriber, but fiber
transmission into the home is now a significant presence in many areas.
A final important application of optical fiber is for local area networks.
Standards have been developed and products introduced for optical fiber networks
that have a total capacity of up to 100 Gbps and can support thousands of stations in
a large office building or a complex of buildings.

## Slide 50
Single-mode Transmission - a single transmission path exists, the distortion found in multimode cannot occur; faster
Multimode transmission - multiple propagation paths exist,
each with a different path length; slower.
Light from a source enters the cylindrical glass or plastic core.
Rays at shallow angles are reflected and propagated along the fiber; other rays are absorbed by the surrounding material.
Notes: Figure 4.7 shows the principle of optical fiber transmission. Light from a source
enters the cylindrical glass or plastic core. Rays at shallow angles are reflected and
propagated along the fiber; other rays are absorbed by the surrounding material.
This form of propagation is called step-index multimode , referring to the variety of
angles that reflect. With multimode transmission, multiple propagation paths exist,
each with a different path length and hence time to traverse the fiber. This causes
signal elements (light pulses) to spread out in time, which limits the rate at which
data can be accurately received. Put another way, the need to leave spacing between
the pulses limits data rate. This type of fiber is best suited for transmission over very
short distances. When the fiber core radius is reduced, fewer angles will reflect. By
reducing the radius of the core to the order of a wavelength , only a single angle or
mode can pass: the axial ray. This single-mode propagation provides superior performance
for the following reason. Because there is a single transmission path with
single-mode transmission, the distortion found in multimode cannot occur. Single
mode is typically used for long-distance applications, including telephone and cable
television. Finally, by varying the index of refraction of the core, a third type of
transmission, known as graded-index multimode , is possible. This type is intermediate
between the other two in characteristics. The higher refractive index (discussed
subsequently) at the center makes the light rays moving down the axis advance
more slowly than those near the cladding. Rather than zig-zagging off the cladding,
light in the core curves helically because of the graded index, reducing its travel distance.
The shortened path and higher speed allows light at the periphery to arrive at
a receiver at about the same time as the straight rays in the core axis. Graded-index
fibers are often used in LANs.

## Slide 52: Wireless Transmission Frequencies
1GHz to 40GHz
Referred to as microwave frequencies
Highly directional beams are possible
Suitable for point to point transmissions
Also used for satellite communications
3 x 1011 to 2 x 1014
Infrared portion of the spectrum
Useful to local point-to-point and multipoint applications within confined areas
30MHz to 1GHz
Suitable for omnidirectional applications
Referred to as the radio range
Three general ranges of frequencies are of interest for wireless transmission.
Notes: Three general ranges of frequencies are of interest in our discussion of wireless transmission. Frequencies in the range of about 1 GHz (gigahertz = 109 hertz) to 40 GHz are referred to as microwave frequencies. At these frequencies, highly directional beams are possible, and microwave is quite suitable for point-to-point transmission. Microwave is also used for satellite communications. Frequencies in the range of 30 MHz to 1 GHz are suitable for omnidirectional applications. We refer to this range as the radio range.
Another important frequency range, for local applications, is the infrared portion of the spectrum. This covers, roughly, from 3 ´ 1011 to 2 ´ 1014 Hz. Infrared is useful to local point-to-point and multipoint applications within confined areas, such as a single room.
For unguided media, transmission and reception are achieved by means of an antenna. Before looking at specific categories of wireless transmission, we provide a brief introduction to antennas.

## Slide 53: Wireless Communication Model
A simple Model of Wireless Communication System:
The transmitting Antenna converts Electrical Signals into Radio Signals
The receiving Antenna converts Radio Signals back to Electrical Signals

## Slide 54: Radiation Pattern
Direction and propagation of a wave depends on antenna shape
Isotropic antenna
  Power propagates in all directions equally (spherical pattern, ideal)
Omni-directional antenna
  Power propagates in all directions on one plane (donut)
Directional antenna
  Power concentrated in particular direction
Notes: An antenna radiates power in all directions but, typically, does not perform equally well in all directions. A common way to characterize the performance of an antenna is the radiation pattern, which is a graphical representation of the radiation properties of an antenna as a function of space coordinates. The simplest pattern is produced by an idealized antenna known as the isotropic antenna. An isotropic antenna is a point in space that radiates power in all directions equally. The actual radiation pattern for the isotropic antenna is a sphere with the antenna at the center.

## Slide 55: Antenna Gain
A measure of the directionality of an antenna
Defined as the power output in a particular direction versus that produced by an isotropic antenna
Measured in decibels (dB)
The increased power radiated in a given direction is at the expense of other directions
Effective area of an antenna is related to the physical size of the antenna and to its shape
GdB = 10 log (P2/P1)
G : Antenna gain,
P1 : Radiated power of the directional antenna, and
P2 : Radiated power from the reference antenna.
For example, if an antenna has a gain of 3 dB, that antenna improves upon the isotropic antenna in that direction by 3 dB.
Power output in a particular direction
VS
Power produced by an isotropic antenna.
Notes: Antenna gain is a measure of the directionality of an antenna. Antenna gain is defined as the power output, in a particular direction, compared to that produced in any direction by a perfect omnidirectional antenna (isotropic antenna). Specifically, GdB = 10 log (P2/P1), where G is the antenna gain, P1 is the radiated power of the directional antenna, and P2 is the radiated power from the reference antenna. For example, if an antenna has a gain of 3 dB, that antenna improves upon the isotropic antenna in that direction by 3 dB, or a factor of 2. The increased power radiated in a given direction is at the expense of other directions. In effect, increased power is radiated in one direction by reducing the power radiated in other directions. It is important to note that antenna gain does not refer to obtaining more output power than input power but rather to directionality. Defined as the power output in a particular direction versus that produced by an isotropic antenna
A concept related to that of antenna gain is the effective area of an antenna. The effective area of an antenna is related to the physical size of the antenna and to its shape.

## Slide 56: Terrestrial Microwave
Most common type is the parabolic “dish”
Typical size is about 3 m in diameter
Antenna is fixed rigidly and focuses a narrow beam to achieve line-of-sight transmission to the receiving antenna
Usually located at substantial heights above ground level
A series of microwave relay towers is used to achieve long-distance transmission
Notes: The most common type of microwave antenna is the parabolic
“dish.” A typical size is about 3 m in diameter. The antenna is fixed rigidly
and focuses a narrow beam to achieve line-of-sight transmission to the receiving
antenna. Microwave antennas are usually located at substantial heights above
ground level to extend the range between antennas and to be able to transmit over
intervening obstacles. To achieve long-distance transmission, a series of microwave
relay towers is used, with point-to-point microwave links strung together over the
desired distance.

## Slide 57: Terrestrial Microwave Applications
Used for long haul telecommunications service as an alternative to coaxial cable or optical fiber
Used for both voice and TV transmission
Fewer repeaters but requires line-of-sight transmission
1-40 GHz frequencies, with higher frequencies having higher data rates
Main source of loss is attenuation caused mostly by distance, rainfall and interference
Notes: The primary use for terrestrial microwave systems is in long haul telecommunications service, as an alternative to coaxial cable or optical fiber. The microwave facility requires far fewer amplifiers or repeaters than coaxial cable over the same distance, but requires line-of-sight transmission. Microwave is commonly used for both voice and television transmission.
Another increasingly common use of microwave is for short point-to-point links between buildings. This can be used for closed-circuit TV or as a data link between local area networks. Short-haul microwave can also be used for the so-called bypass application. A business can establish a microwave link to a long-distance telecommunications facility in the same city, bypassing the local telephone company.
Another important use of microwave is in cellular systems, examined in Chapter 10.
Microwave transmission covers a substantial
portion of the electromagnetic spectrum. Common frequencies used for transmission
are in the range 1 to 40 GHz. The higher the frequency used, the higher the
potential bandwidth, and therefore the higher the potential data rate.

## Slide 58: Satellite Microwave
A communication satellite is, in effect, a microwave relay station
Used to link two or more ground stations
Receives transmissions on one frequency band, amplifies or repeats the signal, and transmits it on another frequency
  Frequency bands are called transponder channels
Notes: A communication satellite is, in effect, a microwave relay station. It is used to link two or more ground-based microwave transmitter/receivers, known as earth stations, or ground stations. The satellite receives transmissions on one frequency band (uplink), amplifies or repeats the signal, and transmits it on another frequency (downlink). A single orbiting satellite will operate on a number of frequency bands, called transponder channels, or simply transponders.

## Slide 59
Two common configurations for satellite communication:
The satellite is being used to provide a point-to-point link between two distant ground-based antennas.
The satellite provides communications between one ground-based transmitter and a number of ground-based receivers.
Two satellites using the same frequency band, if close enough together, interfere with each other.
To avoid this, current standards require a 4° spacing (angular displacement as measured from the earth) in the 4/6-GHz band and a 3° spacing at 12/14 GHz.
No# of possible satellites is quite limited.
Notes: Figure 4.9 depicts in a general way two common configurations for satellite communication. In the first, the satellite is being used to provide a point-to-point link between two distant ground-based antennas.In the second, the satellite provides communications between one ground-based transmitter and a number of ground-based receivers.
For a communication satellite to function effectively, it is generally required that it remain stationary with respect to its position over the earth. Otherwise, it would not be within the line of sight of its earth stations at all times. To remain stationary, the satellite must have a period of rotation equal to the earth's period of rotation. This match occurs at a height of 35,863 km at the equator.
Two satellites using the same frequency band, if close enough together, interfere with each other. To avoid this, current standards require a 4° spacing (angular displacement as measured from the earth) in the 4/6-GHz band and a 3° spacing at 12/14 GHz. Thus the number of possible satellites is quite limited.

## Slide 60
  Ground wave propagation follows the contour of the earth and can propagate distances well over the visual horizon
  This effect is found in frequencies up to about 2MHz
  The best known example of ground wave communication
    is AM radio
Notes: Ground wave propagation (Figure 4.11a) more or less follows the contour of the earth and can propagate considerable distances, well over the visual horizon. This effect is found in frequencies up to about 2 MHz. Several factors account for the tendency of electromagnetic wave in this frequency band to follow the earth's curvature. One factor is that the electromagnetic wave induces a current in the earth's surface, the result of which is to slow the wavefront near the earth, causing the wavefront to tilt downward and hence follow the earth's curvature. Another factor is diffraction, which is a phenomenon having to do with the behavior of electromagnetic waves in the presence of obstacles. Electromagnetic waves in this frequency range are scattered by the atmosphere in such a way that they do not penetrate the upper atmosphere.
The best-known example of ground wave communication is AM radio.

## Slide 61
  Sky wave propagation is used for amateur radio and international broadcasts such as BBC and Voice of America
  A signal from an earth based antenna is reflected from the ionized layer of the upper atmosphere back down to earth
  Sky wave signals can travel through a number of hops, bouncing back and forth between the ionosphere and the earth’s surface
Notes: Sky wave propagation is used for amateur radio and international broadcasts such as BBC and Voice of America. With sky wave propagation, a signal from an earth-based antenna is reflected from the ionized layer of the upper atmosphere (ionosphere) back down to earth. Although it appears the wave is reflected from the ionosphere as if the ionosphere were a hard reflecting surface, the effect is in fact caused by refraction. Refraction is described subsequently.
A sky wave signal can travel through a number of hops, bouncing back and forth between the ionosphere and the earth's surface (Figure 4.11b). With this propagation mode, a signal can be picked up thousands of kilometers from the transmitter.

## Slide 62
  Ground and sky wave propagation modes do not operate above 30MHz - communication must be by line of sight
Notes: Above 30 MHz, neither ground wave nor sky wave propagation modes operate, and communication must be by line of sight( Figure 4.11c). For satellite communication, a signal above 30 MHz is not reflected by the ionosphere and therefore a signal can be transmitted between an earth station and a satellite overhead that is not beyond the horizon. For ground-based communication, the transmitting and receiving antennas must be within an effective line of sight of each other. The term effective is used because microwaves are bent or refracted by the atmosphere. The amount and even the direction of the bend depend on conditions, but generally microwaves are bent with the curvature of the earth and will therefore propagate farther than the optical line of sight.

## Slide 64: Thank You