## Slide 1: Data Communication CSE 315
Dr. A.K.M. Muzahidul Islam
Professor
Computer Science & Engineering (CSE)
United International University (UIU)
Fall 2018

## Slide 2: Resources
Data Communications and Networking. Behrouz A. Forouzan “Chapter 10”
https://www.youtube.com/watch?v=oA7GMmZuexo – Parity Checksum , CRC
https://www.youtube.com/watch?v=T2cmKG1ax08 – CRC
https://www.youtube.com/watch?v=0CLTy231Hsw – FEC

## Slide 3: Outline
Error Detection
Error Correction

## Slide 4
Basic concepts
Networks must be able to transfer data from one device to another with complete accuracy.
Data can be corrupted during transmission.
For reliable communication, errors must be detected and corrected.
Error detection and correction are implemented either at the data link layer or the transport layer of the OSI model.

## Slide 5
Types of Errors

## Slide 6
Single-bit error

## Slide 7
Single bit errors are the least likely type of errors in serial data transmission because the noise must have a very short duration which is very rare. However this kind of errors can happen in parallel transmission.
Example:
If data is sent at 1Mbps then each bit lasts only 1/1,000,000 sec. or 1 μs.
For a single-bit error to occur, the noise must have a duration of only 1 μs, which is very rare.

## Slide 8
Burst error

## Slide 10
The term burst error means that two or more bits in the data unit have changed from 1 to 0 or from 0 to 1.
Burst errors does not necessarily mean that the errors occur in consecutive bits, the length of the burst is measured from the first corrupted bit to the last corrupted bit. Some bits in between may not have been corrupted.

## Slide 11
Burst error is most likely to happen in serial transmission since the duration of noise is normally longer than the duration of a bit.
The number of bits affected depends on the data rate and duration of noise.
Example:
If data is sent at rate = 1Kbps then a noise of 1/100 sec can affect 10 bits.(1/100*1000)
If same data is sent at rate = 1Mbps then a noise of 1/100 sec can affect 10,000 bits.(1/100*106)

## Slide 12: Error detection
Error detection means to decide whether the received data is correct or not without having a copy of the original message.
Error detection uses the concept of redundancy, which means adding extra bits for detecting errors at the destination.
Error Detection Schemes
  Parity Check
  Two-Dimensional Parity Check
  Checksum
  Cyclic Redundancy Check (CRC)-The most Powerful error-detecting code
Notes: Make sense of message.
Make sense of message.

## Slide 13
Parity Check
(Parity Bit)
Append a parity bit to the end of a block of data
Parity uses XOR
Even Parity
  Check Even number of 1s
  Tx (1100011) ->11000110 (0 is appended since even number of 1s)
  Tx (1100001) ->11000011 (1 is appended since odd number of 1s))
Odd Parity
  Check Odd number of 1s
  Tx (0110011) ->01100111 (1 is added)
  Tx (0100011) ->01000110 (0 is added)
However, if Two (or any even number) of bits are inverted due to error, an undetected error occurs.

## Slide 14
Two-Dimensional Parity Bit
The string of data bits to be checked is arranged in a two-dimensional array.
Calculate Row parity check (VRC) and Column parity check (LRC) and the resulted message is transmitted.
Example (2-D Even Parity Scheme):
  1100111 | 1
  1011101 | 1 Row parity check (VRC)
  0111001 | 0
  0101001 | 1
  ---------------
  0101010 | 1 Column parity check (VRC)
Original Data:
Without parity check
Final Data to be transmitted includes
Row parity check
Column parity check

## Slide 15
  Transmitted Blocks:
  1100111 | 1
  1011101 | 1 Row parity check
  0111001 | 0
  0101001 | 1
  ---------------
  0101010 | 1 Column parity check
  Received Blocks:
  1100111 | 1 2D can detect errors until 3 bits.
  1001001 | 1 Four errors in the transmitted block
  0111001 | 0 s.t. two bits in one block is damaged and
  0111101 | 1 two bits of the same position in
  --------------- another block damaged. Then 2D parity
  0101010 | 1 check cannot detect errors.

## Slide 16
Checksum
Transmitting Side
1100
0010
+ 1100
1000
---------------
0010 0010
Receiving Side
  0010 0010
  + 1011 (Checksum)
  ----------------------
  0010 1101
0010
0010
------
0100
Flip -> 1011 (Checksum)
0010
1101
------
1111
Flip -> 0000 (Correct)

## Slide 17: Error Correction
It can be handled in two ways:
receiver can have the sender retransmit the entire data unit.
The receiver can use an error-correcting code, which automatically corrects certain errors.
Error Detection Scheme
  Forward Error Correction (FEC)

## Slide 18: Forward Error Correction (FEC)
Using Haming Distance
Haming Distance
  Two bit set of same length
  V1 = 011011 and V2 = 110001
  d(V1, V2) = 3 (011011 - 110001) – different

## Slide 19
  Instead of sending two bit set of data covert into codeword (e.g. 5-bit)
Data Codeword
00 00000
01 00111 Codeword must be known
10 11001 if 5 bits => 2^5 possible codewords
11 11110
Tx Data = 01
Tx Codeword = 00111 -> Rx (received)
Errors - ?

## Slide 20
Redundancy

## Slide 21: Cyclic Redundancy Check (CRC)
Polynomial x^4 + x^2 + x + 1
Tx and Rx agree on Generator Polynomial
The degree of the Generator Polynomial is the size of the CRC i.e. CRC = 4
Given:
  Message M(x) = 10110101110
  Generator Polynomial G(x) = 1101 i.e. x ^3 + x^2 + 0 + x^0
  CRC is then = 3 since x ^3 + x^2 + 0 + x^0

## Slide 22
Perform
  Message M(x) XOR 1101 G(x)
  i.e. 1 – 1 and 0 – 0 = 0
  1 – 0 and 0 – 1 = 1

## Slide 24: Thank You