## Slide 1
United International University
Computer Networks Laboratory
CSE 324
Azim Uddin Chowdhury
UIU CISCO Networking Academy
Phone: 01741125920
Mail: azim.cy@gmail.com
FaceBook Group: www.facebook.com/groups/CN324
OR,
Computer Networks Lab (CISCO)

## Slide 2: Decimal and Binary conversion
Notes: Section 1.2.1.5

## Slide 3: Internet Protocol (IP)
Type of IP:
 IPv4: Internet Protocol version 4
            IPv4 Length: 32 bits
 IPv6: Internet Protocol version 6
            IPv6 Length: 128 bits
IPv4 : Dotted Decimal Address
Ex. 192.168.10.0/24
IPv6 : Hexadecimal Address separated by colons (:)
Ex. 2001:0db8:85a3:0000:0000:8a2e:0370:7334/64
Notes: Section 1.2.1.5

## Slide 4: Internet Protocol version 4 (IPv4) : Public
Class | Start IP | End IP | Network Part | Host Part | Default Subnet Mask
A | 0.0.0.0 | 127.255.255.255 | 8 | 24 | 255.0.0.0
B | 128.0.0.0 | 191.255.255.255 | 16 | 16 | 255.255.0.0
C | 192.0.0.0 | 223.255.255.255 | 24 | 8 | 255.255.255.0
D | 224. 0.0.0 | 239.255.255.255 | Reserved for Multicasting |  | 
E | 240.0.0.0 | 255. 255.255.254 | Experimental; used for research |  | 
Notes: Section 1.2.1.5

## Slide 5: Internet Protocol version 4 (IPv4) : Public
Special Use:
Network Address: All Host bits are ‘0’
Broadcast Address: All Host bits are ‘1’
Loopback Address:
IPv4: 127.0.0.1/8 & IPv6: ::1
Link Local Address:
    IPv4: 169.254.0.1/16 & IPv6: FE80::1
Notes: Section 1.2.1.5

## Slide 6: Internet Protocol version 4 (IPv4) : Private
Class | Start IP | End IP | Network Part | Host Part | Default Subnet Mask
A | 10.0.0.0 | 10.255.255.255 | 8 | 24 | 255.0.0.0
B | 172.16.0.0 | 172.31.255.255 | 16 | 16 | 255.255.0.0
C | 192.168.0.0 | 192.168.255.255 | 24 | 8 | 255.255.255.0
IP Address:
Network Address: All Host bits are ‘0’
Subnet Mask: All Network bits are ‘1’
Broadcast Address: All Host bits are ‘1’
Notes: Section 1.2.1.5

## Slide 7: Internet Protocol version 4 (IPv4)
Network Address: All Host bits are ‘0’
Subnet Mask: All Network bits are ‘1’
Broadcast Address: All Host bits are ‘1’
Class:
Default Network Address:
Default Subnet Mask:
Default Broadcast Address:
Subnet/Borrow Bit:
Prefix:
Network Address:
Custom Subnet Mask:
1st IP Address: Last IP Address:
Notes: Section 1.2.1.5

## Slide 8: Internet Protocol version 4 (IPv4)
Notes: Section 1.2.1.5