## Slide 1: Data Communication CSE 315
Dr. A.K.M. Muzahidul Islam
Professor
Computer Science & Engineering (CSE)
United International University (UIU)
Fall 2018

## Slide 2: Outline
Information Theory
Entropy

## Slide 3: Information Theory
The basic goal of a transmission system
  Transmit message from source to destination
    Source : generates signal
      To achieve maximum amount of information to transmit usually some processing is done at the sender end (i.e. between source and channel)
    Channel : convey that signal to the destination
  Source -> Processing -> Channel -> Receiver -> Destination
1948 C. Shannon “A Mathematical Theory of Communication”
  Made the breakthrough contribution in the area of communication.
  The maximum rate at which one can transmit data through a channel
  The minimum rate at which one can compress a source
As per Shannon the Processing Block is divided into two parts
  Source Coding
  Channel Coding
  Information Source -> Source Encoder -> Channel Encoder ->
  Channel ->
  Channel Decoder -> Source Decoder -> Destination

## Slide 4
I = log2 (1 / P)
  If P is high then I is low
  If P is low then I is high
Unit of information depends upon the base of log
  If base is 2 then unit is bit
  If base is e then unit is nat
  If base is 10 then unit is decit

## Slide 5: Information
Equation of
  I(p) = logb (1/p) or
  I(p) = - logb (1/p)
p = probability of the event happening
b = base (base 2 is mostly used in information theory)
unit of information is determined by base
  base 2 = bits
  base 3 = trits
  base 10 = decits
  base e = nats

## Slide 6: Exercises
Example of Calculating Information Coin Toss
  There are two probabilities in fair coin, which are Head(0.5) and Tail(0.5).
  Answer: Thus, if you get either head or tail you will get 1 bit of information through following formula.
  I(H) = log2 (1/0.5) = 1 bit
  I(T) = log2 (1/0.5) = 1 bit
  H-Head and T-Tail

## Slide 7
2. Example of Balls in the bin
  Let’s consider a bin that is populated with nine balls of three different colors namely red, yellow and green. Among them if there are 4 red balls, 3 green balls and 2 yellow balls, what are the information that you will get by choosing a ball from the bin?
  Answer:
  I(red ball) = log2(1/ (4/9)) = 1.1699 bits
  I(yellow ball) = log2(1/(2/9)) = 2.1699 bits
  I(green ball) = log2(1/(3/9)) = 1.58496 bits

## Slide 8: Entropy
What if we want to measure what are overall uncertainty for an information source where the probability of outcomes are unequal?
The name of this measurement is Entropy.
Entropy is simply the average(expected) amount of the information we receive every time we get the symbol (message) from an information source.
H(X) = Σ pi log2 (1/pi)
OR
H(X) = - Σ pi log2 (pi)
i=M
i=1
i=M
i=1

## Slide 9: Entropy (Cont’d)
Entropy is simply the average(expected) amount of the information from the event.
H(X) = Σ pi log2 (1/pi)
OR
H(X) = - Σ pi log2 (pi)
i=M
i=1
i=M
i=1

## Slide 10: Exercise
3. Find entropy of a random variable
Let’s consider a random variable X which takes four values a, b, c, and d with probabilities of 1/2, 1/4, 1/8, and 1/8.
What is its entropy?
What is the maximum information that this random variable could have?

## Slide 11
4. Calculate the entropy of Balls in the bin
  Let’s consider a bin that is populated with nine balls of three different colors namely red, yellow and green. Among them if there are 4 red balls, 3 green balls and 2 yellow balls. What is expected amount of information each time you choose a ball from the bin?
  Answer:
  H(X) = - (4/9) log(4/9) + -(2/9) log(2/9) + - (3/9) log(3/9) = 1.5304755
  Therefore, you are expected to get 1.5304755 information each time you choose a ball from the bin

## Slide 12
5. Calculate the entropy of transmitted messages
  Three messages m1, m2, and m3 are transmitted over a channel and their probabilities are ½, ¼, and ¼, respectively. Calculate the entropy.
  Answer:
  H(X) = 3/2 bits

## Slide 13: Properties
H(x) ≥ 0
H(x) = Σ pi log2 (1/pi) ≥ 0
H(x) ≤ Lavr < H(x) + 1
Lavr –Average code length of a source code
i=M
i=1
Notes: 01818630083

## Slide 15: Resources
Information Theory Basics
file:///Users/muzahidul/Downloads/InfoTheoryBookChapter01.pdf
Probability and Entropy
http://csustan.csustan.edu/~tom/sfi-csss/info-theory/info-lec.pdf
https://www.csun.edu/~twang/595DM/Slides/Information%20&%20Entropy.pdf
Information Theory Video
https://www.youtube.com/watch?v=nvmo9voRiSs&t=1830s

## Slide 16: Thank You